## Slide 1: Reading Component Datasheets
ENGS 28 · Day 5X — In-Class

## Slide 2: Embedded systems need peripherals
A microcontroller on its own senses nothing and drives nothing.
Every useful system connects the MCU to the world through input and output components.
Sensors, switches, and data streams feed in; the MCU drives displays, actuators, and data streams out.
Inputs feed the MCU through interfaces; the MCU sends commands out through interfaces on the other side.

## Slide 3: Only the datasheet can answer these
What supply voltage does it need — and what min/max conditions can it tolerate?
What signal does it produce or consume, and what does that signal represent?
Does it do its own conversion and give you numbers over I²C, or output a raw voltage your ADC must interpret?
How do you wire it up, and what must your code configure before it responds?
Datasheets are dense and written for experts — but they follow a predictable structure. Learn where to look and you can navigate any of them.

## Slide 4: Every datasheet has the same skeleton
First page — Features (what it does) and Description (always read this — names the interface and application).
Pinout / Pin descriptions — which pin is which.
Absolute Maximum Ratings — never exceed; doing so destroys the part.
Recommended Operating Conditions — the range it's designed for.
Electrical Characteristics — voltages, currents, timing, with Min / Typ / Max columns.
Application Information — the designer's goldmine: example schematics, register maps, usage notes.
Packaging — physical dimensions (rarely needed for breadboards).
Watch for active-low: a bar over a pin name (or a star in a table) means you pull it to ground to activate it.

## Slide 5: Datasheet Scavenger Hunt
Notes: Suggested timing: ≈ 45 min.

## Slide 6: Your table gets one component
Open its datasheet from Canvas, display it on your table's monitor, and complete the Datasheet Passport (next slides).
Be ready to share your answers with the class in the last five minutes.
Possible components: TMP235 (analog temp sensor), CdS photocell (light-dependent resistor), LSM303AGR (I²C accel/mag), HT16K33 (I²C LED-matrix driver), and others as assigned.
Some questions have analog and digital versions — answer the one that applies. Finish early? Sketch the hookup to the STM32 on your board.

## Slide 7: Activity: Datasheet Passport — Part A: What Is It?
These answers are on the first page.
Read the Description (not the Features list). In one sentence, what does this component do?
Find the Recommended Operating Conditions. What supply voltage range (VDD/VCC) does it accept? Is 3.3 V within range? (Passive part? Find the max rated voltage and power dissipation instead.)
Find the Absolute Maximum Ratings. What is the maximum voltage the part can survive? Any other limits a careless user might exceed?

## Slide 8: Activity: Datasheet Passport — Part B: How Does It Communicate?
These answers are in the Pinout and Application sections.
What interface does it use? Check one or more: passive (variable resistance), analog voltage output, I²C, SPI, UART/serial, PWM input, other.
List every pin needed for a minimal hookup. For each, write its name and what it connects to (VDD, GND, a specific STM32 pin, etc.).

## Slide 9: Activity: Datasheet Passport — Part C: What Does It Output or Require?
These answers are in the Electrical Characteristics table. Answer the version that matches your component.
Passive sensor: resistance at min/max of the range? Linear, or is there a curve/formula?
Analog output: output voltage at min/max? Linear? Write the transfer function (voltage → physical value).
I²C: what address(es) can it use? List them (base address plus A0/A1 pins).
SPI: what mode (CPOL/CPHA) and max clock frequency?
All: max supply current? Does that rule out powering it from a GPIO pin (max 25 mA)? (Passive: max power dissipation instead.)

## Slide 10: Activity: Datasheet Passport — Part D: Making It Work
These answers are in the Application Information section.
Find the example schematic. Sketch the minimal hookup on your board — power, ground, signal lines, labeled with pin names.
Name one thing you'd configure or calculate in code before reading data (set I²C address, choose a gain, apply a conversion formula, …).
What was the most confusing or surprising thing you found?
Part E — Group Slide: add one slide for your component to the shared class deck (Canvas) with your Part A–D answers (not the sketch). Short phrases, not paragraphs.

## Slide 11: Share-Out
Each table presents their slide in 30 seconds or less. Cover at least:
  Component name and what it does (one sentence).
  Interface type: passive, analog, I²C, SPI, or other.
  One thing that surprised you or that others should know.
As you listen, note which components are analog and which are digital — you'll use several of these parts later in the course.